New Video ASIC
John P. Doty
Noqsi Aerospace Ltd
December 6, 2012

---
Two CCD Pixels
- Reset pulse is very noisy (ignore data)
- Reference level varies pixel to pixel (“kTC” noise)
- Subtract filtered reference level from filtered video level (“correlated double sampling”) to get best estimate of charge.

---
ΔΣ Principle
- First-order ΔΣ “modulator”.
  - Integrate the difference between input and output.
  - Mean density of “1” bits in output will then approximate the input.
- Difference between instantaneous output (“1” or “0”) and mean output is considered “modulator noise”.

---
Noise Shaping
- Substitute higher-order low pass filter for integrator.
  - Stronger feedback at low frequencies forces modulator noise to higher frequencies.
    - Fewer samples needed for high precision.
  - Care needed to avoid instability.

---
ΔΣ Signal Processing for CCD Video
- Clamp phase – reset ΔΣ modulator, force reference level to approximately zero.
- Deintegrate phase – process samples with negative weight to subtract residual reference level.
- Integrate phase – process samples with positive weight to estimate video charge.
- Finish phase – ignore input (zero weight), run modulator to obtain estimate of remaining modulator digitization error.
  - MND02 needed long finish phase, extending into next pixel → even/odd modulator pairs.
    - New ASIC does not need this.

---
Changes in new ASIC
- Fourth order modulator ( second order for MND02)
  - Better precision from fewer samples
- Both modulator and bias dac use 1.2V reference.
  - MND02 needed 0.2V for modulator.
- Single-ended circuits with higher voltage swing, 1.2V
  - MND02 used differential circuits with 0.4V swing

---
Design Tools
- "Delta-Sigma Modulators: Modeling, Design, and Applications" by Bourdopoulos, Pnevmatikakis, Anastassopoulos, and Deliyannis.
  - Modulator architecture.
  - Optimized Z-domain transfer functions.
- Mathematica
  - Solve for filter coefficients given transfer function parameters.
  - Simulation of idealized modulator.
  - Modeling with linear algebra.
- gEDA/ngspice
  - Schematic capture
  - SPICE netlisting
    - New netlister “spice-noqsi” allows control of net scope, reducing clutter.
  - Simulation

---
MND02 Modulator
Z transform representation
Z-1 indicates a one sample delay
1/(1-Z-1) indicates integration.

---
Modulator for new ASIC
j1= k1=0.389887	j2= k2=0.355616
j3= k3=0.484287	j4= k4=0.366992
c1= c2=c3=0.25	g1= 0.00730082 g2=0.0467911

---
Decimation
- Turn output bit stream to a measured number
- For first order ΔΣ modulator, just average the bits.
- For higher order, a weighted average is needed.
  - Depends on input noise spectrum and modulator noise shaping.
- Implemented downstream in FPGA, not part of ASIC, but must have filter coefficients to analyze simulations.

---
Decimation filter weights from linear algebra and simulation
- Very similar appearance
  - Simulation poorly constrains first few coefficients.

---
Modulator linearity and residuals
- Simulation with kTC noise, but no other input noise. No even/odd (49 total clock cycles)
  - Stable to ±0.6 of nominal full scale
  - (peak-peak signal)/(RMS noise) > 4000

---
Circuit Blocks
- OpenIP
  - Mainly for digital and I/O
- Custom
  - InverterX
    - CMOS inverter used as fast amplifier
  - Q2V
    - Charge integrator
  - V2Q
    - Delay-free charge input (chopped)
  - ClockGen
    - Non-overlapping clocks
  - Comparator
  - Polarity
    - Voltage polarity switch

---
ClockGen Simulation

---
Polarity Switch Simulation

---
Question on Next Steps
- Do we need filter resonance (g coefficients)?
  - Tuned to a particular number of samples/pixel.
  - Signal/(modulator noise) ~2000 at 50 samples/pixel without resonance, ~4000 with resonance.
  - Difficult to design very weak feedback here, probably need significant power.